## Slide 1
NETCONF / YANG
Overview
a

## Slide 2: Session Objectives
At the end of this presentation, you will be able to:
  Identify the major problems/issues facing network administrators
  Describe the NETCONF/YANG protocol and modeling language
  Describe how the features of NETCONF/YANG address major problems in network administration
  Describe a use case for NETCONF/YANG

## Slide 3: Outline
NETCONF/YANG
  Definition
  Distinction between Protocol and Modeling language
  NETCONF Protocol Layers
  NETCONF Operations
    Base
    Capabilities
Solutions for Network Managers
Problems for Network Managers
Summary

## Slide 4: Network Management Problems Needing Solutions
I must configure everything manually from the CLI. I need a programmatic interface!
All devices have a different syntax or operations!
I can’t tell the difference between configuration and operational data!
I need to be able to configure services on the network and not just individual devices!
If I hit an error while configuring one of several devices, I must go back and reconfigure all devices back to the way they were!
I cannot test a configuration before committing it!
You will learn to overcome these problems in this training using NETCONF/YANG

## Slide 5: NETCONF and YANG
NETCONF
YANG
Protocol to install, manipulate, and delete the configuration of network devices
RPC-based with XML-based data encoding
Data modeling language to model configuration, state data and operations
Mappings to NETCONF and RESTCONF (draft)

## Slide 6: A Data Model and a Protocol
YANG: A Data Model
Explicitly and precisely determines the structure, syntax and semantics of the data…
…that is externally visible
Consistent and complete
NETCONF: A Protocol
Provides primitives to view and manipulate data
Encoding of the data as defined by the data model
Data
Model
Instance
Data
Protocol

## Slide 7: Terminology
Client
Server
Session
Datastore
Configuration Data
State Data
NETCONF
Manager
Yang
Models
Management
Applications
YANG Modules
YANG Modules
YANG Modules
YANG
Modules
NETCONF

## Slide 8: NETCONF Layering Model
Operations
<get>
<get-config>
Content
Configuration
data
Notification
data
Messages
<rpc>
<notification>
Secure
Transport
ssh
NETCONF
Layer
Example
<rpc xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<get-config>
<source>
<running/>
</source>
</get-config>
</rpc>

## Slide 9: NETCONF and YANG Architecture
Client
Content
Operations
RPC
Transport
Modeled in YANG
Content
Operations
RPC
Transport
Server
Configuration
Data Storage
NETCONF
NETCONF

## Slide 10: NETCONF Operations
Base Operations
Additional Operations (Capabilities)
<rpc message-id="101"
xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
    <get-config>
      <source>
      <running/>
      </source>
    </get-config>
</rpc>
Content
Operations
RPC
Transport

## Slide 11: Base Operations
Data Manipulation
<get>
<get-config>
<edit-config>
<copy-config>
<delete-config>
Session Management
<close-session>
<kill-session>
Base NETCONF specification provides restricted set of operations
Additional operations are defined as capabilities
Locking
<lock>
<unlock>

## Slide 12: NETCONF Capabilities
Example:
:candidate,
:writable-running,
:startup
Configuration loaded by the device at startup
Complete and active configuration
Working copy to manipulate with no impact on current configuration
Capabilities supporting multiple configuration datastores
  Additional operations and content supported on a device
Candidate
Running
Startup
<copy>
<commit>
<copy>

## Slide 13: Advertising Capabilities
Capabilities are advertised by server and client at start of session
<hello xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<capabilities>
<capability>urn:ietf:params:netconf:base:1.1</capability>
<capability>urn:ietf:params:netconf:capability:startup:1.0</capability>
</capabilities>
<session-id>4</session-id>
</hello>
Client
Server

## Slide 14: Network Management Problems Needing Solutions
I must configure everything manually from the CLI. I need a programmatic interface!
All devices have a different syntax or configuration file!
I can’t tell the difference between config and state data!
I need to be able to configure a service on the network and not individual devices!
If I hit an error while configuring one of several devices, I must go back and reconfigure all devices back to the way they were!
I cannot test a configuration before committing it!
Notes: Everything must be configured manually from CLI
  Manually configuring from Excel, Word or printed doc
All devices have a different syntax or configuration file
  No common database schema
It is Hard to figure out what I can manage
  No distinction between config and state data
I need to configure a service on the network not individual devices
  Unable to configure multiple devices concurrently
If I find an error while configuring several devices, I must go back and reconfigure all devices back to the way they were
  No automantic rollback if something fails
I cannot test a configuration before implementing it
  There is no sandbox to test or validate

## Slide 15: I must configure everything manually from the CLI. I need a programmatic interface!
NETCONF provides the fundamental programming features for comfortable and robust automation of network services
Scripting can be done via Python or PERL
<rpc message-id="101“ xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<copy-config>
<target>
<stamrtup/>
</target>
<source>
<running/>
</source>
</copy-config>
</rpc>

## Slide 16: All devices seem to have a different syntax or configuration file!
There is a single standard IETF XML configuration schema to upload/download regardless of device.
Modeled in YANG
Human readable, easy to learn
Hierarchical configuration data models
Reusable types and groupings (structured types)
Extensibility through augmentation
Formal constraints validation
Modular (modules and sub-modules)
Well defined versioning rules

## Slide 17: I can’t tell the difference between config and state data!
YANG Models clearly divided into Configuration and State Datastores
Complete bank of configurable elements downloadable in a single transaction
Base Operations:
<get-config> Retrieve all configuration data*
<get> Retrieve all configuration +state data*
* Can be filtered to retrieve a subset

## Slide 18: I need to be able to configure a service on the network and not individual devices!
NETCONF provides primitives to:
In parallel:
Acquire locks on multiple devices
Upload configuration changes
Change running configuration and test
Make changes permanent
Release locks

## Slide 19: If I hit an error while configuring one of several devices, I must go back and reconfigure all devices back to the way they were!
Capability Operation
:confirmed-commit <cancel-commit>
Transactions can be atomic – either it completely succeeds or there is no change!
This gives you the ability to “UNDO”

## Slide 20: I cannot test a configuration before implementing it!
Capability Operation
:confirmed-commit <validate>
You can check a complete configuration for syntactical and semantic errors before applying the configuration to the device
Candidate
validate
<validate>
  <source>
    <candidate/>
  </source>
</validate>

## Slide 21: Use Case:
Need to program:
Task 1: Activate interface on group of devices
Task 2: Assign addresses to interfaces
Task 3: Configure MPLS VPN Tunnel
Router 1:
FastEth0: 2001:db8:c18:1::3/128
Router 2:
FastEth0: 2001:db8:c18:1::2/128

## Slide 22: Summary
NETCONF provides the fundamental programming features for comfortable and robust automation of network services
YANG is a full, formal contract language with rich syntax and semantics to build applications on